## Slide 1
A Computer Architecture Workshop:
Visions for the Future
Celebrating Yale@75
September 19th, 2014
Trevor Mudge
The University of Michigan, Ann Arbor

## Slide 2: Visions for the Future?
We need to think out-of-the-box
Get back to the basics of computing
Do something radical
Get rid of the von Neumann straight jacket
Our abstractions don’t expose the basic logical fabic
I propose the following: Let’s take a leaf from toys—LEGO
There’s a solution that’s been with us a long time....
It’s a basic building block that digital systems can be constructed from
No –not a NAND gate
It has a higher level of abstraction

## Slide 3: The Universal Logic Module—ULM

## Slide 4: Golden Age—Dennard Scaling Worked
About every 2 years we got:
2× area
40% increase in frequency
50% reduction in power
No change in power density
1
Notes: If s is the linear dimension scaling factor ≈ √2
Device dimension tox, L, W 1/s
Voltage V 1/s
Current I 1/s
Capacitance εA/t 1/s
Delay VC/I 1/s
Power VI 1/s2
Power density VI/A 1

## Slide 5: Turn of the Century
Cracks appeared
First crack: frequency scaling became a problem
  Vdd got stuck & power density started to creep up
  Clock frequency could no longer be a selling point
  Core count was the new metric
Later:
  Each new tech node no longer showed power and frequency scaling
  Node numbers became symbolic names —still followed the 1/√2× sequence
  Only area shrank with new nodes
8 64-bit cores

## Slide 6: What About Cost?
Two Views
Intel
Everyone else
  cost per transistor reached a minimum at 28 nm
Notes: Qulcomm nvidia imec...

## Slide 7: Where Does That Leave Us
No “new” technology that looks promising
  Cheap
  Reliable
  Support density
Can’t see much beyond 7 years
  But where’s the capital investment?
From a computer architect’s viewpoint
Fast complex cores have been explored
Multiple cores are being explore
  Unlikely to reach large numbers except for data centers / HPC
Application domain specific architectures look promising
  Gpu led the way
  Only so many applications that warrant specialization

## Slide 8: Some Opportunities
Memory—new interesting technologies
  3D monolithic FLASH
  Various NV-memory technologies
Advanced packaging
  3D die stacking
  Interposers
Longer time horizon
3D monolithic ICs
—see FLASH
High Bandwidth Memory

## Slide 9: FIN